## Slide 1: ECE 498AL Programming Massively Parallel Processors Lecture 6: CUDA Memories Part 2

## Slide 2: Tiled Multiply
Md
Nd
Pd
Pdsub
TILE_WIDTH
WIDTH
WIDTH
TILE_WIDTH
TILE_WIDTH
bx
tx
0
1
TILE_WIDTH-1
2
0
1
2
by
ty
2
1
0
TILE_WIDTH-1
2
1
0
TILE_WIDTH
TILE_WIDTH
TILE_WIDTHE
WIDTH
WIDTH
Break up the execution of the kernel into phases so that the data accesses in each phase is focused on one subset (tile) of Md and Nd

## Slide 3: A Small Example
Pd1,0
Md2,0
Md1,1
Md1,0
Md0,0
Md0,1
Md3,0
Md2,1
Pd0,0
Md3,1
Pd0,1
Pd2,0
Pd3,0
Nd0,3
Nd1,3
Nd1,2
Nd1,1
Nd1,0
Nd0,0
Nd0,1
Nd0,2
Pd1,1
Pd0,2
Pd2,2
Pd3,2
Pd1,2
Pd3,1
Pd2,1
Pd0,3
Pd2,3
Pd3,3
Pd1,3

## Slide 4: Every Md and Nd Element is used exactly twice in generating a 2X2 tile of P
P0,0 thread0,0 | P1,0 thread1,0 | P0,1 thread0,1 | P1,1 thread1,1
M0,0 * N0,0 | M0,0 * N1,0 | M0,1 * N0,0 | M0,1 * N1,0
M1,0 * N0,1 | M1,0 * N1,1 | M1,1 * N0,1 | M1,1 * N1,1
M2,0 * N0,2 | M2,0 * N1,2 | M2,1 * N0,2 | M2,1 * N1,2
M3,0 * N0,3 | M3,0 * N1,3 | M3,1 * N0,3 | M3,1 * N1,3
Access
order

## Slide 5: Breaking Md and Nd into Tiles
Pd1,0
Md2,0
Md1,1
Md1,0
Md0,0
Md0,1
Md3,0
Md2,1
Pd0,0
Md3,1
Pd0,1
Pd2,0
Pd3,0
Nd0,3
Nd1,3
Nd1,2
Nd1,1
Nd1,0
Nd0,0
Nd0,1
Nd0,2
Pd1,1
Pd0,2
Pd2,2
Pd3,2
Pd1,2
Pd3,1
Pd2,1
Pd0,3
Pd2,3
Pd3,3
Pd1,3
Break up the inner product loop of each thread into phases
At the beginning of each phase, load the Md and Nd elements that everyone needs during the phase into shared memory
Everyone access the Md and Nd elements from the shared memory during the phase

## Slide 6: Each phase of a Thread Block uses one tile from Md and one from Nd
 |  |  |  | Step 4 | Step 5 | Step 6
T0,0 | Md0,0 ↓ Mds0,0 | Nd0,0 ↓ Nds0,0 | PValue0,0 += Mds0,0*Nds0,0 + Mds1,0*Nds0,1 | Md2,0 ↓ Mds0,0 | Nd0,2 ↓ Nds0,0 | PValue0,0 += Mds0,0*Nds0,0 + Mds1,0*Nds0,1
T1,0 | Md1,0 ↓ Mds1,0 | Nd1,0 ↓ Nds1,0 | PValue1,0 += Mds0,0*Nds1,0 + Mds1,0*Nds1,1 | Md3,0 ↓ Mds1,0 | Nd1,2 ↓ Nds1,0 | PValue1,0 += Mds0,0*Nds1,0 + Mds1,0*Nds1,1
T0,1 | Md0,1 ↓ Mds0,1 | Nd0,1 ↓ Nds0,1 | PdValue0,1 += Mds0,1*Nds0,0 + Mds1,1*Nds0,1 | Md2,1 ↓ Mds0,1 | Nd0,3 ↓ Nds0,1 | PdValue0,1 += Mds0,1*Nds0,0 + Mds1,1*Nds0,1
T1,1 | Md1,1 ↓ Mds1,1 | Nd1,1 ↓ Nds1,1 | PdValue1,1 += Mds0,1*Nds1,0 + Mds1,1*Nds1,1 | Md3,1 ↓ Mds1,1 | Nd1,3 ↓ Nds1,1 | PdValue1,1 += Mds0,1*Nds1,0 + Mds1,1*Nds1,1
Phase 1
Phase 2
time

## Slide 7: Tiled Matrix Multiplication Kernel
__global__ void MatrixMulKernel(float* Md, float* Nd, float* Pd, int Width)
{
1. __shared__float Mds[TILE_WIDTH][TILE_WIDTH];
2. __shared__float Nds[TILE_WIDTH][TILE_WIDTH];
3. int bx = blockIdx.x; int by = blockIdx.y;
4. int tx = threadIdx.x; int ty = threadIdx.y;
// Identify the row and column of the Pd element to work on
5. int Row = by * TILE_WIDTH + ty;
6. int Col = bx * TILE_WIDTH + tx;
7. float Pvalue = 0;
// Loop over the Md and Nd tiles required to compute the Pd element
8. for (int m = 0; m < Width/TILE_WIDTH; ++m) {
// Coolaborative loading of Md and Nd tiles into shared memory
9. Mds[ty][tx] = Md[Row*Width + (m*TILE_WIDTH + tx)];
Nds[ty][tx] = Nd[Col + (m*TILE_WIDTH + ty)*Width];
__syncthreads();
11. for (int k = 0; k < TILE_WIDTH; ++k)
Pvalue += Mds[ty][k] * Nds[k][tx];
Synchthreads();
}
13. Pd[Row*Width+Col] = Pvalue;
}

## Slide 8: CUDA Code – Kernel Execution Configuration
// Setup the execution configuration
dim3 dimBlock(TILE_WIDTH, TILE_WIDTH);
dim3 dimGrid(Width / TILE_WIDTH,
Width / TILE_WIDTH);

## Slide 9: First-order Size Considerations in G80
Each thread block should have many threads
  TILE_WIDTH of 16 gives 16*16 = 256 threads
There should be many thread blocks
  A 1024*1024 Pd gives 64*64 = 4096 Thread Blocks
  TILE_WIDTH of 16 gives each SM 3 blocks, 768 threads (full capacity)
Each thread block perform 2*256 = 512 float loads from global memory for 256 * (2*16) = 8,192 mul/add operations.
  Memory bandwidth no longer a limiting factor

## Slide 10: Tiled Multiply
Md
Nd
Pd
Pdsub
TILE_WIDTH
WIDTH
WIDTH
TILE_WIDTH
TILE_WIDTH
bx
tx
0
1
TILE_WIDTH-1
2
0
1
2
by
ty
2
1
0
TILE_WIDTH-1
2
1
0
TILE_WIDTH
TILE_WIDTH
TILE_WIDTHE
WIDTH
WIDTH
Each block computes one square sub-matrix Pdsub of size TILE_WIDTH
Each thread computes one element of Pdsub
m
k
bx
by
k
m

## Slide 11: G80 Shared Memory and Threading
Each SM in G80 has 16KB shared memory
  SM size is implementation dependent!
  For TILE_WIDTH = 16, each thread block uses 2*256*4B = 2KB of shared memory.
  The shared memory can potentially have up to 8 Thread Blocks actively executing
    This allows up to 8*512 = 4,096 pending loads. (2 per thread, 256 threads per block)
    The threading model limits the number of thread blocks to 3 so shared memory is not the limiting factor here
  The next TILE_WIDTH 32 would lead to 2*32*32*4B= 8KB shared memory usage per thread block, allowing only up to two thread blocks active at the same time
Using 16x16 tiling, we reduce the accesses to the global memory by a factor of 16
  The 86.4B/s bandwidth can now support (86.4/4)*16 = 347.6 GFLOPS!

## Slide 12: Tiled Matrix Multiplication Kernel
__global__ void MatrixMulKernel(float* Md, float* Nd, float* Pd, int Width)
{
1. __shared__float Mds[TILE_WIDTH][TILE_WIDTH];
2. __shared__float Nds[TILE_WIDTH][TILE_WIDTH];
3. int bx = blockIdx.x; int by = blockIdx.y;
4. int tx = threadIdx.x; int ty = threadIdx.y;
// Identify the row and column of the Pd element to work on
5. int Row = by * TILE_WIDTH + ty;
6. int Col = bx * TILE_WIDTH + tx;
7. float Pvalue = 0;
// Loop over the Md and Nd tiles required to compute the Pd element
8. for (int m = 0; m < Width/TILE_WIDTH; ++m) {
// Coolaborative loading of Md and Nd tiles into shared memory
9. Mds[ty][tx] = Md[Row*Width + (m*TILE_WIDTH + tx)];
Nds[ty][tx] = Nd[Col + (m*TILE_WIDTH + ty)*Width];
__syncthreads();
11. for (int k = 0; k < TILE_WIDTH; ++k)
Pvalue += Mds[ty][k] * Nds[k][tx];
Synchthreads();
}
13. Pd[Row*Width+Col] = Pvalue;
}

## Slide 13: Tiling Size Effects
Notes: Mention that we’re limited from large tile sizes by thread context maximums.

## Slide 14: Summary- Typical Structure of a CUDA Program
Global variables declaration
  __host__
  __device__... __global__, __constant__, __texture__
Function prototypes
  __global__ void kernelOne(…)
  float handyFunction(…)
Main ()
  allocate memory space on the device – cudaMalloc(&d_GlblVarPtr, bytes )
  transfer data from host to device – cudaMemCpy(d_GlblVarPtr, h_Gl…)
  execution configuration setup
  kernel call – kernelOne<<<execution configuration>>>( args… );
  transfer results from device to host – cudaMemCpy(h_GlblVarPtr,…)
  optional: compare against golden (host computed) solution
Kernel – void kernelOne(type args,…)
  variables declaration - __local__, __shared__
    automatic variables transparently assigned to registers or local memory
  syncthreads()…
Other functions
  float handyFunction(int inVar…);
repeat
as needed